## Slide 1: CAD/CAM

## Slide 2: Scope of CAD/CAM

## Slide 3: CAD/CAM system
Today, almost all the CAD/CAM software systems are interactive. To use this kind of system well, one, as a designer or user, should know of how these systems work and how to set or get information with CAD/CAM system through GUI(Graphics User Interface)

## Slide 4: CAD

## Slide 5: Instruction to computer graphics
Computer graphics focuses mainly on displays of any digital image by a computer.
There are bunch of hardware and software developed for fast and correct displays of graphics on terminals.
The core techniques of computer graphics are based on geometry, optics, physics, and perception.

## Slide 6: Coordinate system

## Slide 7: Three types of coordinate system
Coordinate systems are the most important concept in a CAD system. They are used to input, store, and display geometric model. There are three kinds of coordinate systems,
Model coordinate system (MCS)
Working coordinate system (WCS)
Screen coordinate system (SCS)

## Slide 8: Model Coordinate System (MCS)
MCS is a 3D Cartesian coordinate system used by most of CAD softwares to perform internal geometrical data operations, such as record, storage and calculation.
MCS is the only coordinate system CAD software can identify. Even users define another type of coordinate system during the process of creating models, the model will still be convert to data under MCS to store.
Sometime MCS is also called Absolute Coordinate System(ACS).

## Slide 9: Working Coordinate System(WCS)
A modelling processing of a 3D body is usually a result of combining many steps of creating some simple structure bodies. WCS is an user defined local coordinate system, with which user can generate some basic structures easily.
WCS has different appearances in different CAD systems. One of the most useful one is a sketch plane.
As we mentioned, whatever was chosen to be a coordinate system , the stored data should be represented with MCS. To satisfy this requirement, a homogenous transform matrix will play an very important role.

## Slide 10: Working Coordinate System(WCS)
Given a vector under WCS, , and let is the stored point represented with MCS. Supposing T is the transformation matrix, we have

## Slide 11: Homogenous transformation matrix
Since we still need consider translation and project operation meanwhile. The matrix to finish all the transformations from WCS to MCS looks like as follows.

## Slide 12: Homogenous transformation matrix
Let
The above matrix become
T is to transform coordinate components, o means origin point shifting,
p is perspective vector, s means perspective shifting

## Slide 13: Homogenous transformation
Actually, for any point under WCS should be transformed to MCS, the final forms looks like

## Slide 14: Some useful HT matrices
Matrix without perspective involved

## Slide 15: Some useful HT matrices
Matrix pure shearing involved
At the same time, T part of this matrix is symmetric. Which means t21=t12, t31=t13, t32=t23

## Slide 16
Example: Given a cube with length of edge 1 at the origin O, assume vertex O is fixed, and there is a homogenous transformation which shear vertex F(1,1,1) to F’(1,1,2). Find out the transformation matrix and the new positions of all vertices.

## Slide 17
To vertex E, we have the linear equations after taking use of shearing transformation
The solution of homogenous transformation matrix is

## Slide 18: Screen coordinate system (SCS)
The coordinate system of screen is a 2D Cartesian coordinate system, which origin (0,0) locates at left-upper corner of the screen. The scale of SCS usually depends on the resolution of screen. For example if the revolution of a screen is 1096x1024, which means the X axis extend to right of screen until scale of 1096, and the Y axis extend to bottom of screen until scale of 1024.
The SCS is mainly used to display correct images on screen device. So it is pixel related.
X
Y
(0,0)

## Slide 19: Coordinate system
By default, in most of CAD software, the WCS and MCS are overlapped as you start up the main program.
Definitely, To display correct image of the cad model on screen, we still need some transformation operations to make it sense.
From the view of user, the inputted geometrical elements will firstly transform to uniforms under MCS, then through display converting package developed by CAD software provider, all 3D geometrical items will be shown on the 2D screen.

## Slide 20: CAD data exchange and storage

## Slide 21: CAD data exchange and storage
Graphic standard
  There are various CAD software systems used in different fields. How people could share the same model among these systems? The answer to share data obeying the same standard. The mainstream data standards are: GKS,STEP

## Slide 23: Data exchange standards
There is increasing application of CAD accompanied by a growth in product variety and the range of companies involved
  component suppliers must often match their designs to many variants of different products
  a large amount of component and product data must be exchanged
  the simplest way is for both companies to used same CADCAM system and software revision number
  however, it is more equitable for different CADCAM systems to accurately exchange the same data
    too many individual inter-software translator programs would be required
    need to convert the data into a neutral file format first
    then translate the neutral format into the target system data structure
However, a neutral file format is not straightforward due to
  different international CADCAM methods
  different CAD representations:
    2D draughting; wire frame geometry; surface/solid models
    higher order curves → cubic polynomial conversion leads to loss of precision
Ongoing effort to define an internationally accepted standard

## Slide 24: IGES
Initial Graphics Exchange Specification
– this is a standard for th structure and syntax of neutral file in ASCII, compressed
ASCII or binary format
• the ASCII format is: 80 character records/lines, terminated by semicolons, fields divided with commas
• Start section:
– contains data such as the features of the originating system to assist the
recipient in translating the file
• Global section:
– contains 24 parameter fields which are necessary to translate the file
• Directory section:
– contains 18 x 8-character fields on 2 lines as an entry for each entity; codes
represent the entity type, subtype, and pointers to entity data in next section
• Parameter Data Section:
– contains entity specific data such as coordinates, annotations, spline control
points, pointers to directory entries, etc.
• the first parameter for each entry identifies the entity type from which the meanings for remaining
parameters are derived.
• Termination Section:
– marks the end of the data file, contains subtotals of records for data transmission
checks

## Slide 25: IGES data types
The global section consists of:
  delimiter characters (1,2); sender’s identifier (3); filename (4); software ID (5); IGES processor version (6); number precision (7-11); receiver’s identifier (12); model space scale (13); units (14); unit name (15); maximum number of line thicknesses (16); maximum line thickness (17); time file generated (18); smallest distance (19); largest coordinate (20);
Each record line has an identifier in columns 73-80 used as a pointer for cross-referencing between sections
  the first character indicates the section (S = Start, G = Global, D = Directory, P = Parameter, T = Termination)

## Slide 26: IGES example
EXAMPLE IGES FILE S0000001
1H,,1H;,,,9HMASTERCAM, 1H1,16,8,24,8,56,,1.,1,4HINCH,1,0.01, G0000001
13H850101.0100000,0.,100.,,,,; G0000002
116 1 1 1 1 0 00000000D0000001
116 0 3 1 D0000002
124 2 1 1 1 0 00000000D0000003
124 0 3 1 D0000004
100 3 1 1 1 3 00000000D0000005
100 0 3 1 D0000006
110 4 1 1 1 0 00000000D0000007
110 0 3 1 D0000008
116,100.,-100.,0.; 1P0000001
124,1.,0.,0.,0.,0.,1.,0.,0.,0.,0.,1.,0.; 3P0000002
100,0.,100.,-100.,-150.,-100.,150.,-99.99999; 5P0000003
110,135.3553,-135.3553,0.,206.066,-64.64465,0.; 7P0000004
S0000001G0000002D0000008P0000004 T0000001
• (116) point, (124) transformation matrix, (100) circular arc, (110) line
Note: Parameter entry for line (110) is x1, y1, z1, x2, y2, z2; for arc (100) is z,
x, y of centre, x, y of start point, x, y of end point; for point (116) is x, y, z.

## Slide 27: STEP
Standard for the Exchange of Product model data
Uses a formal model for data exchange, described using an information modelling language called EXPRESS
STEP has a three layer architecture enabling definition of multiple application views and implementations:
  techniques for implementing STEP, relations between EXPRESS language, model, and the physical file
  resource information models to provide context independent information
description of geometry, topology, product structure
  application protocols describing constrained subsets related to specific applications such as geometry, electrical product modelling, etc.

## Slide 28: EXPRESS language
IGES defines the file format
STEP uses the EXPRESS language to map the data to the physical file
the EXPRESS language is used to define entities as a collection of attributes
  – strings
  – real/integer numbers
  – logical/Boolean values
  – references to other entities, etc.
collections of attributes may be:
  – ordered: arrays, lists
  – unordered: sets, bags
the collection of entity definitions, data types and associated constraints is a schema

## Slide 29: EXPRESS geometric entities
EXPRESS-G is a specific subset of EXPRESS used for graphical notation
  – simpler definition of relationships between entities in a class hierarchy
  – constraints cannot be specified
  – other EXPRESS subsets developed
ENTITY point ;
  x-coordinate : REAL ;
  y-coordinate : REAL ;
  z-coordinate : REAL ;
END_ENTITY ;
ENTITY circle ;
  centre : point ;
  radius : REAL ;
END_ENTITY ;
#15 = POINT (3.3,4.4,5.5) ;
#16 = POINT (6.6,7.7,8.8) ;
#17 = CIRCLE (#15, 5.0) ;

## Slide 30: STEP standard
STEP is being developed incrementally as a series of separate standards (parts) divided into classes:
  – Introductory (1-9)
    • Part 1: Overview and general Principles
  – Description Methods (11-19)
    • Parts 11, 12: EXPRESS language
  – Implementation Methods (21-29)
    • describe how EXPRESS mapped to physical files and other storage mechanisms
  – Conformance Testing Methodology and Framework (31-39)
    • provide methods for testing implementations, and test suites
  – Integrated Resources (41-99, 101-199)
    • geometry and structure representation (41-99), and widely used applications such as draughting and FE (101-199)
  – Application Protocols (210-299)
    • implementation of STEP to specific industrial applications
  – Abstract Test Suites (301-399)
    • for each of the application protocols
  – Application Interpreted Constructs (501-?)
    • describe model entity constructs and specific modelling approaches

## Slide 31: STEP
Standard for the Exchange of Product Model Data ( STEP), officially the ISO standard 10303, Product Data Representation and Exchange, is a series of international standards with the goal of defining data across the full engineering and manufacturing life cycle. The ability to share data across applications, across vendor platforms and between contractors, suppliers and customers, is the main goal of this standard.

## Slide 32: STEP
The broad scope of STEP is as follows.
1. The standard method of representing the information necessary for completely defining a product throughout its entire life, i.e., from the product conception to the end of useful life.
2. Standard methods for exchanging the data electronically between two different systems.
The STEP documentation is split into eight major areas.

## Slide 33: The STEP documentation is split into eight major areas.
Overview It gives the general introduction and overview of the standard and forms part one of the ISO standard 10303.
Description Methods The application protocols planned in STEP are far reaching compared to any other existing standard or models. Hence, a new descriptive formal information modelling language called EXPRESS is developed such that the protocols be properly defined
Implementation Methods This provides specifications as to how the STEP information be physically represented for the exchange environment.

## Slide 34
Conformance and Tools This part provides the specifications for conformance testing of the processors used for STEP information. They provide information on methods for testing of software-product conformance to the STEP standard, guidance for creating abstract-test suites and the responsibilities of testing laboratories. The STEP standard is unique in that it places a very high emphasis on testing and actually includes these methods in the standard.
Integrated-generic Resources These contain the specifications of the information models that support various application areas that form part of STEP. The topics that form part of this specification are: geometric and topological representation, product structure organisation, materials, visual presentation, tolerances, form features and process structure and properties.

## Slide 35
Application Information Models These specify the information models to be used for specific application areas such as draughting, finite element analysis, kinematics, building core model and Engineering analysis core.
Application Protocols These are the main protocols to be used as subsets of STEP information model for exchange of data between specific application systems (such as between two finite element systems or between a CAD and Process Planning system).

## Slide 36
Application Interpreted Constructs These relate to the specific resources useful for defining the generic structures useful for applications. These are reusable groups of information resource entities that make it easier to express identical semantics in more than one application protocol. Examples include edge-based wireframe, draughting elements, constructive solid geometry, etc. onwards. Examples include edge-based wireframe, shell-based wireframe, geometry-bounded 2D wireframe, draughting annotation, drawing structure and administration, draughting elements, geometry-bounded surface, non-manifold surface, manifold surface, geometry-bounded wireframe, etc.
Application Protocols These define the context for the use of product data for a specific industrial need. These are more complex data models used to describe specific product-data applications. These parts are known as application protocols and describe not only what data is to be used in describing a product, but how the data is to be used in the model. The application protocols use the integrated information resources in well defined combinations and configurations to represent a particular data model of some phase of product life.

## Slide 37
Data storage
  Most of CAD/CAM software systems store the data of model by relational database.

## Slide 38: Exporting CAD data
Transferring 3D CAD models between different software packages can be challenging
  – fortunately, most CAD packages will directly import files produced in most other packages
• If the file type is not supported, the data must be exported as a neutral format and then imported
  – important information may be “lost in translation”
  – this applies especially to non-geometric data in 3D models, such as material type
• The geometry may not be properly converted
  – e.g. only the individual entities are exported/imported, ignoring surface details or topology
  – try exporting some simple 3D geometry from SolidWorks into different neutral file formats (DXF, IGES, STEP) and reimporting them

## Slide 39: Introduction to Geometric Modelling
Usually, geometric modelling is a combination discipline with applied mathematics and computational geometry. In this discipline, people designed varied algorithms to describe all kinds of shapes by computers.
Building two or three dimensional models is crucial content of CAD & CAM.

## Slide 40: Geometry of curve
Standard mathematic curves
Bezier curves
B-spline curves
Parameterized curves
Wire frame modelling

## Slide 41: Geometry of surface
Ruled surfaces
Other standard mathematical surfaces
NURBS
Surface modelling

## Slide 42: Boolean operations in CSG

## Slide 43: Constructive solid geometry (CSG)
CSG is one of a fundamental theories of varies 3D modelling CAD system.
Boolean operations of multi-bodies
  One of ideas in CSG is that some algebraic calculations can be performed between two bodies.
  There are three basic Boolean operations of bodies, which are named unite, difference and intersect, derived from set theory. However, in Solidworks, they are called add, subtract and common, respectively.
  Through Boolean operations one can take uses of several bodies to generate a new body.

## Slide 44: Boolean operations in set theory
In set theory, we have

## Slide 45: Boolean operations of multi-bodies
Target: The body with the finished geometry is called the target;
Tool: The body used to create or edit the shape is called the tool.

## Slide 46: Boolean logic with binary tree
A binary tree structure is usually used to store the basic bodies one lead nodes, the operations on the internal nodes, and the final body on the root node.

## Slide 47: Three methods to create 3D models

## Slide 48: Primitive method
  In the method, any 3D model was divided into several simple, basic, standard of items, such as blocks, cylinders, spheres, cones, etc. which usually integrated in CAD system as a standard body. Through these, user can decide how to combine different of them together to construct a new model, then using Boolean operations to get the final result.

## Slide 50: Feature method
  Let user to utilize some predefined feature generating instruments, like groove, hole, slot, boss, pad, etc. to simulate a real manufacturing process to create some structure from a simple basic body.

## Slide 51: Sketch method
  The main idea of this approach is to create 3D body by 2D sketch. Taking use of extrusion, revolution algorithms, in addition some of basic Boolean operations, use can create a very complex 3D structures.
  This method is the most popular way used by most of commercial CAD softwares including Solidworks.

## Slide 52: Sketch method
The main steps of sketch method to create 3D models are
  Define a sketch plane as cross section;
  Sketch 2D shapes on the cross section;
  Constraint 2D shapes with accurate dimensions;
  Perform 2D to 3D operations.

## Slide 53: Key disciplines of modelling in Solidworks

## Slide 54: Key disciplines of modelling in Solidworks
For basic bodies, generate 3D model by taking use of 2D shapes;
Combine basic bodies to create a complex body;
Repeated bodies can be made through array operations;

## Slide 55: Coordinate system
Coordinate systems are the most important concept in a CAD system. They are used to input, store, and display geometric model. There are three kinds of coordinate systems, that is, model coordinate system (MCS), working coordinate system (WCS), and screen coordinate system (SCS).
By default, there are already a coordinates system provided for user by SOLIDWORKS every time you open a new modelling project. Usually, at the lower-left corner of the canvas, you can notice the symbol of coordinate system with three axes.
Whenever user need to carry on some location or orientation related modelling steps, the coordination system should be considered.
For example, in the scenarios of re-oriented a model or two models comparing user should define his own reference coordinate systems.

## Slide 56: References objects
Reference points
Reference vectors/axes
Reference plane

## Slide 57: Sketch
Plane curves
Two types of Constraint
  Dimensional constraints: length and angle
  Geometric constraints: parallel, perpendicular, normal, tangent, concentric, etc.

## Slide 58: CAM

## Slide 59: Brief
Scope and applications
  NC in CAM
  Principal types of CNC machine

## Slide 60: Machine tools
tools and their construction features
  tooling for CNC – ISO designation for
tooling
  CNC operating system
  FANUC, SINUMERIK – LINUMERIK.

## Slide 61: Introduction to CAPP
Three main parameters to define a machining process
Principles for process design
Processing planning systems

## Slide 62: Programming for CNC machining
Coordinate systems of CNC
Manual part
Computer assisted part programming
CNC part programming with CAD system.

## Slide 63: Material handling in CAM environment
Logistic and storage system
  AGVS
  AS/RS
  Swarf handling and disposal of wastes
Assembly lines
  Quantitative analysis of assembly systems.

## Slide 64: Key disciplines of manufacturing under Solidworks environment
Configuration for a mill or turn machine
Features to machining strategy
Generate operation plan
Generate tool path
Simulation
Post process

## Slide 65: The following slides are only for learning purpose

## Slide 66
Create a new part
Check the unit setting
Using sketch to create part body
  Smart dimension is an import tool to drive the model creatation

## Slide 67
Go to the Solidworks CAM module(just perform each of tool button alone the toolbar from left to right, one can finally get the tool path and G-codes)
  Define machine
  Setup coordinate system
  Define stock size using stock manager

## Slide 68
  Using setup->mill setup to tell the machine which direction is the machining (removing material) direction.
  Extract machinable features(which features will be removed)
  Generate operation plan(usually have cutting times for the same surface)
    Adjust the plan by removing part of operations or changing some parameters for cutting
    How to decide the basic cutting parameters(F/S):
      Cutting and spindle speed calculations

## Slide 69
          Feed rate calculatons
            Ususlly, we have general start conditons, in which
            For HSS(high speed steel tool)

## Slide 70
        For Carbide
        Depth of cut is approximately 10% the diameter of the tool, except with face mills:0.005 inch max. (SFPM=surface feet per minute)
      Decide roughing