## Slide 1: CAD/CAM

## Slide 2: Scope of CAD/CAM

## Slide 3: CAD/CAM system
Today, almost all the CAD/CAM software systems are interactive. To use this kind of system well, one, as a designer or user, should know of how these systems work and how to set or get information with CAD/CAM system through GUI(Graphics User Interface)

## Slide 5: CAD

## Slide 6: Instruction to computer graphics
Computer graphics focuses mainly on displays of any digital image by a computer.
There are bunch of hardware and software developed for fast and correct displays of graphics on terminals.
The core techniques of computer graphics are based on geometry, optics, physics, and perception.

## Slide 7: Coordinate system

## Slide 8: Three types of coordinate system
Coordinate systems are the most important concept in a CAD system. They are used to input, store, and display geometric model. There are three kinds of coordinate systems,
Model coordinate system (MCS)
Working coordinate system (WCS)
Screen coordinate system (SCS)

## Slide 9: Model Coordinate System (MCS)
MCS is a 3D Cartesian coordinate system used by most of CAD softwares to perform internal geometrical data operations, such as record, storage and calculation.
MCS is the only coordinate system CAD software can identify. Even users define another type of coordinate system during the process of creating models, the model will still be convert to data under MCS to store.
Sometime MCS is also called Absolute Coordinate System(ACS).

## Slide 10: Working Coordinate System(WCS)
A modelling processing of a 3D body is usually a result of combining many steps of creating some simple structure bodies. WCS is an user defined local coordinate system, with which user can generate some basic structures easily.
WCS has different appearances in different CAD systems. One of the most useful one is a sketch plane.
As we mentioned, whatever was chosen to be a coordinate system , the stored data should be represented with MCS. To satisfy this requirement, a homogenous transform matrix will play an very important role.

## Slide 11: Working Coordinate System(WCS)
Given a vector under WCS, , and let is the stored point represented with MCS. Supposing T is the transformation matrix, we have

## Slide 12: Homogenous transformation matrix
Since we still need consider translation and project operation meanwhile. The matrix to finish all the transformations from WCS to MCS looks like as follows.

## Slide 13: Homogenous transformation matrix
Let
The above matrix become
T is to transform coordinate components, o means origin point shifting,
p is perspective vector, s means perspective shifting

## Slide 14: Homogenous transformation
Actually, for any point under WCS should be transformed to MCS, the final forms looks like

## Slide 15: Some useful HT matrices
Matrix without perspective involved

## Slide 16: Some useful HT matrices
Matrix pure shearing involved
At the same time, T part of this matrix is symmetric. Which means t21=t12, t31=t13, t32=t23

## Slide 17
Example: Given a cube with length of edge 1 at the origin O, assume vertex O is fixed, and there is a homogenous transformation which shear vertex F(1,1,1) to F’(1,1,2). Find out the transformation matrix and the new positions of all vertices.

## Slide 18
To vertex E, we have the linear equations after taking use of shearing transformation
The solution of homogenous transformation matrix is

## Slide 19: Screen coordinate system (SCS)
The coordinate system of screen is a 2D Cartesian coordinate system, which origin (0,0) locates at left-upper corner of the screen. The scale of SCS usually depends on the resolution of screen. For example if the revolution of a screen is 1096x1024, which means the X axis extend to right of screen until scale of 1096, and the Y axis extend to bottom of screen until scale of 1024.
The SCS is mainly used to display correct images on screen device. So it is pixel related.
X
Y
(0,0)

## Slide 20: View Generation
The display screen is two-dimensional.
How to present 3D model on the screen.
the orthogonal projection.

## Slide 21: Coordinate system
By default, in most of CAD software, the WCS and MCS are overlapped as you start up the main program.
Definitely, To display correct image of the cad model on screen, we still need some transformation operations to make it sense.
From the view of user, the inputted geometrical elements will firstly transform to uniforms under MCS, then through display converting package developed by CAD software provider, all 3D geometrical items will be shown on the 2D screen.

## Slide 22: CAD data exchange and storage

## Slide 23: CAD data exchange and storage
Graphic standard
  There are various CAD software systems used in different fields. How people could share the same model among these systems? The answer is to share data obeying the same standard. The mainstream data standards are: GKS,STEP, etc.

## Slide 24: Data exchange standards
There is increasing application of CAD accompanied by a growth in product variety and the range of companies involved
  component suppliers must often match their designs to many variants of different products
  a large amount of component and product data must be exchanged
  the simplest way is for both companies to used same CADCAM system and software revision number
  however, it is more equitable for different CADCAM systems to accurately exchange the same data
    too many individual inter-software translator programs would be required
    need to convert the data into a neutral file format first
    then translate the neutral format into the target system data structure
However, a neutral file format is not straightforward due to
  different international CADCAM methods
  different CAD representations:
    2D draughting; wire frame geometry; surface/solid models
    higher order curves → cubic polynomial conversion leads to loss of precision
Ongoing effort to define an internationally accepted standard

## Slide 25: IGES(Initial Graphics Exchange Specification)
A standard for the structure and syntax of neutral file in ASCII, compressed ASCII or binary format
the ASCII format is: 80 character records/lines, terminated by semicolons, fields divided with commas
Start section:
  – contains data such as the features of the originating system to assist the recipient in translating the file
Global section:
  – contains 24 parameter fields which are necessary to translate the file
Directory section:
  – contains 18 x 8-character fields on 2 lines as an entry for each entity; codes represent the entity type, subtype, and pointers to entity data in next section
Parameter Data Section:
  – contains entity specific data such as coordinates, annotations, spline control points, pointers to directory entries, etc.
the first parameter for each entry identifies the entity type from which the meanings for remaining parameters are derived.
Termination Section:
  – marks the end of the data file, contains subtotals of records for data transmission checks

## Slide 26: IGES data types
The global section consists of:
  delimiter characters (1,2); sender’s identifier (3); filename (4); software ID (5); IGES processor version (6); number precision (7-11); receiver’s identifier (12); model space scale (13); units (14); unit name (15); maximum number of line thicknesses (16); maximum line thickness (17); time file generated (18); smallest distance (19); largest coordinate (20);
Each record line has an identifier in columns 73-80 used as a pointer for cross-referencing between sections
  the first character indicates the section (S = Start, G = Global, D = Directory, P = Parameter, T = Termination)

## Slide 27: IGES example
EXAMPLE IGES FILE S0000001
1H,,1H;,,,9HMASTERCAM, 1H1,16,8,24,8,56,,1.,1,4HINCH,1,0.01, G0000001
13H850101.0100000,0.,100.,,,,; G0000002
116 1 1 1 1 0 00000000D0000001
116 0 3 1 D0000002
124 2 1 1 1 0 00000000D0000003
124 0 3 1 D0000004
100 3 1 1 1 3 00000000D0000005
100 0 3 1 D0000006
110 4 1 1 1 0 00000000D0000007
110 0 3 1 D0000008
116,100.,-100.,0.; 1P0000001
124,1.,0.,0.,0.,0.,1.,0.,0.,0.,0.,1.,0.; 3P0000002
100,0.,100.,-100.,-150.,-100.,150.,-99.99999; 5P0000003
110,135.3553,-135.3553,0.,206.066,-64.64465,0.; 7P0000004
S0000001G0000002D0000008P0000004 T0000001
• (116) point, (124) transformation matrix, (100) circular arc, (110) line
Note: Parameter entry for line (110) is x1, y1, z1, x2, y2, z2; for arc (100) is z,
x, y of centre, x, y of start point, x, y of end point; for point (116) is x, y, z.

## Slide 28: STEP(Standard for the Exchange of Product model data)
Uses a formal model for data exchange, described using an information modelling language called EXPRESS
STEP has a three layer architecture enabling definition of multiple application views and implementations:
  techniques for implementing STEP, relations between EXPRESS language, model, and the physical file
  resource information models to provide context independent information
description of geometry, topology, product structure
  application protocols describing constrained subsets related to specific applications such as geometry, electrical product modelling, etc.

## Slide 29: EXPRESS language
IGES defines the file format
STEP uses the EXPRESS language to map the data to the physical file
the EXPRESS language is used to define entities as a collection of attributes
  – strings
  – real/integer numbers
  – logical/Boolean values
  – references to other entities, etc.
collections of attributes may be:
  – ordered: arrays, lists
  – unordered: sets, bags
the collection of entity definitions, data types and associated constraints is a schema

## Slide 30: EXPRESS geometric entities
EXPRESS-G is a specific subset of EXPRESS used for graphical notation
  – simpler definition of relationships between entities in a class hierarchy
  – constraints cannot be specified
  – other EXPRESS subsets developed
ENTITY point ;
  x-coordinate : REAL ;
  y-coordinate : REAL ;
  z-coordinate : REAL ;
END_ENTITY ;
ENTITY circle ;
  centre : point ;
  radius : REAL ;
END_ENTITY ;
#15 = POINT (3.3,4.4,5.5) ;
#16 = POINT (6.6,7.7,8.8) ;
#17 = CIRCLE (#15, 5.0) ;

## Slide 31: STEP standard
STEP is being developed incrementally as a series of separate standards (parts) divided into classes:
  – Introductory (1-9)
    • Part 1: Overview and general Principles
  – Description Methods (11-19)
    • Parts 11, 12: EXPRESS language
  – Implementation Methods (21-29)
    • describe how EXPRESS mapped to physical files and other storage mechanisms
  – Conformance Testing Methodology and Framework (31-39)
    • provide methods for testing implementations, and test suites
  – Integrated Resources (41-99, 101-199)
    • geometry and structure representation (41-99), and widely used applications such as draughting and FE (101-199)
  – Application Protocols (210-299)
    • implementation of STEP to specific industrial applications
  – Abstract Test Suites (301-399)
    • for each of the application protocols
  – Application Interpreted Constructs (501-?)
    • describe model entity constructs and specific modelling approaches

## Slide 32: STEP
Standard for the Exchange of Product Model Data ( STEP), officially the ISO standard 10303, Product Data Representation and Exchange, is a series of international standards with the goal of defining data across the full engineering and manufacturing life cycle. The ability to share data across applications, across vendor platforms and between contractors, suppliers and customers, is the main goal of this standard.

## Slide 33: STEP
The broad scope of STEP is as follows.
1. The standard method of representing the information necessary for completely defining a product throughout its entire life, i.e., from the product conception to the end of useful life.
2. Standard methods for exchanging the data electronically between two different systems.
The STEP documentation is split into eight major areas.

## Slide 34: The STEP documentation is split into eight major areas.
Overview It gives the general introduction and overview of the standard and forms part one of the ISO standard 10303.
Description Methods The application protocols planned in STEP are far reaching compared to any other existing standard or models. Hence, a new descriptive formal information modelling language called EXPRESS is developed such that the protocols be properly defined
Implementation Methods This provides specifications as to how the STEP information be physically represented for the exchange environment.

## Slide 35
Conformance and Tools This part provides the specifications for conformance testing of the processors used for STEP information. They provide information on methods for testing of software-product conformance to the STEP standard, guidance for creating abstract-test suites and the responsibilities of testing laboratories. The STEP standard is unique in that it places a very high emphasis on testing and actually includes these methods in the standard.
Integrated-generic Resources These contain the specifications of the information models that support various application areas that form part of STEP. The topics that form part of this specification are: geometric and topological representation, product structure organisation, materials, visual presentation, tolerances, form features and process structure and properties.

## Slide 36
Application Information Models These specify the information models to be used for specific application areas such as draughting, finite element analysis, kinematics, building core model and Engineering analysis core.
Application Protocols These are the main protocols to be used as subsets of STEP information model for exchange of data between specific application systems (such as between two finite element systems or between a CAD and Process Planning system).

## Slide 37
Application Interpreted Constructs These relate to the specific resources useful for defining the generic structures useful for applications. These are reusable groups of information resource entities that make it easier to express identical semantics in more than one application protocol. Examples include edge-based wireframe, draughting elements, constructive solid geometry, etc. onwards. Examples include edge-based wireframe, shell-based wireframe, geometry-bounded 2D wireframe, draughting annotation, drawing structure and administration, draughting elements, geometry-bounded surface, non-manifold surface, manifold surface, geometry-bounded wireframe, etc.
Application Protocols These define the context for the use of product data for a specific industrial need. These are more complex data models used to describe specific product-data applications. These parts are known as application protocols and describe not only what data is to be used in describing a product, but how the data is to be used in the model. The application protocols use the integrated information resources in well defined combinations and configurations to represent a particular data model of some phase of product life.

## Slide 38: Exporting CAD data
Transferring 3D CAD models between different software packages can be challenging
  – fortunately, most CAD packages will directly import files produced in most other packages
• If the file type is not supported, the data must be exported as a neutral format and then imported
  – important information may be “lost in translation”
  – this applies especially to non-geometric data in 3D models, such as material type
• Sometimes, the geometry could not be properly converted

## Slide 39: Introduction to Geometric Modelling
Geometric modelling is a combination discipline with applied mathematics and computational geometry. In this discipline, people designed varied algorithms to describe all kinds of shapes by computers.
Building two or three dimensional models is crucial content of CAD & CAM.
When we were creating a geometric model of a mechanism using a CAD system, what we do is just map real or imaginary structure to a new algorithmic object. This process should be unique and complete. Otherwise, a designer will not be able to restore any of them from start to the end or vice versa. Furthermore, the model could not be manufactured.
This section will tell you what is the theoretical basis of geometric modelling.

## Slide 40: Geometry of curve
Representation of curves
Cubic polynomial curves
Bezier curves
Cubic spline curves
B-spline curves
NURBS

## Slide 41: Geometry of curve – Representation of curves
Issues in CAD of classical analytic curves
  Uneven points
  Numerical issue (infinite slope like…)
  Multi-valued points
  Coordinate system dependent
Solution
  Interpolation (pass through all the points)
  Approximation (the best fit instead of passing through all points)
  Parametrize curve (time-varied trajectory of a moving point)
  Composite (piecewise curve)
Ex.

## Slide 42: Geometry of curve – cubic polynomial curves
Lagrange/Hermite interpolation
For normalize form, t should belong to interval of [0,1], given two end vectors and the end vectors of slope We will solve out
Or
We call the functions of t Hermite basis. The above equation means we can use boundary conditions and Hermite basis to define a cubic polynomial curves

## Slide 43: Geometry of curve – Bezier curves
Definition and Control polygon
Bernstein polynomial
for 4 order, the degree of polynomial n=3. we have
  with matrix representation

## Slide 44: Geometry of curve – Bezier curves
Global control. Changing one of control points affects the shape of whole curve.
The degree of equation depends heavily on the number of control points, which means that the more control points you give, the less efficient it is to generate the curve.

## Slide 45: Geometry of curve – Cubic spline curves
Interpolation by piecewise cubic curve with function of
Requirements:
  Continuous at joint points
  The first and second derivatives are also continuous at joint points
  The second derivative equal to zero at the end of point
Given any three points, there are 8 equations meet the above requirements, which can be solved for 2 cubic curves.
Locally control the shape of curves

## Slide 46: Geometry of curve – B-spline curves
B-spline shorted from Basis Spline, is a generalisation of Bezier curve. In other words, a Bezier is a special case of B-spline.
Separate curve degree from the number of given points, which means B-spline curve has the flexibility of choosing the degree of the curve irrespective of the number of control points.
B-splines can be of any degree, but the degrees 2 or 3 is the most useful in computer graphics.
A B-spline is a smoothly joined piecewise parametric polynomial curve
B-spline can be use as both interpolation and approximation.

## Slide 47: Geometry of curve – B-spline curves
Similar to the form of a Bezier curve, a B-spline uses the basis functions of degree k and n+1 data points to define,
where are the iterated basis functions of order k+1
and

## Slide 48: Geometry of curve – B-spline curves
In above equations, is a component of knot vector with a form of a non-descending sequence
sometimes, through identifying the two end of subinterval, we can collapse it. A designer always adapt collapsing the first of k+1 nots to 0 and the end of k+1 knots to 1 in order to avoid missing curve parts at two ends of knots sequence, we call this kind of knot vector open uniform vector.
Usually, intervals in a knot vector defines all the basis polynomials what we need to construct any spline constrained by control points.
To define a B-spline curve, there are three information should be provided: a degree k, n+1 control points and dimensions knot vector

## Slide 49: Geometry of curve – B-spline curves
For example, given n=3,k=1, T=(0,0,1/3,2/3,1,1) , we have

## Slide 50: Geometry of curve – B-spline curves
pi+1
pi-2
pi-1
pi
pi+2
(1-t)pi-1
tpi
ui-2
ui-1
ui
ui+1
ui+2
ui+3
ui+4
0
r(u)

## Slide 51: Geometry of curve – B-spline curves
pi+1
pi-2
pi-1
pi
pi+2
ui-2
ui-1
ui
ui+1
ui+2
ui+3
ui+4
0
Basis functions

## Slide 52: Geometry of curve – B-spline curves
Given a knot vector (0,0,0,0,1,2,2,2,2), for 0-degree, there are 8 pieces of basis function. For 1-degree there are 7 pieces of basis function, and for 2-degree there are only 6, and so on.
An order k open uniform B-spline with n+1=k points is the Bezier curve of order k.
For a given degree k, the basis functions are simply shifted versions of one another.
0
0
0
0
1
2
2
2
2

## Slide 53: Geometry of curve – NURBS
Any B-spline whose knot vector is neither uniform nor open uniform is non-uniform.
An uniform knot vector example
An open uniform knot vector
A non-uniform knot vector

## Slide 54: Geometry of curve – NURBS
Any basis function can be represented by algebraic ratio of two polynomials is rational, which has a form like
Based on rational basis functions defined on non-uniform knot vector, we get NURBS. It is short of Non-Uniform Rational Basic Spline.

## Slide 55: Geometry of curve – NURBS
NURBS is essentially B-spline in homogeneous coordinates, which is more flexible than B-spline through adding another set of (n+1) weights. Today it is actually an industry standard adopted by most of commercial CAD systems.
NURBS is the general form of the B-spline which incorporate open uniform and uniform B-splines as special cases
Even can be used to approximate a circle with knot vector(0,0,0,1/4,1/4,1/2,1/2,3/4,3/4,1,1,1)

## Slide 56: Geometry of surface
A surface can be represented by both parametric and non-parametric methods.
For non-parametric (also has a name of implicit) representation a surface is defined by a polynomial of three variables as
in discrete situation, the surface will be described by xy grid of size points. Implicit method is more powerful than parametric method because a lot of implicit surfaces don’t have any parametric from. Sometimes we also call implicit surfaces algebraic surfaces.

## Slide 57: Geometry of surface
For parametric representation, a surface is defined by a set of functions, with the form like
If one parameter is fixed a curve will be got. It means with two spatial curves a surface could be built.

## Slide 58: Geometry of surface
There are two types of surface
  Analytical surface
    Plane
    Spherical surface
    Surface of revolution: Generated by revolving a 2D closed curve around an axis. With the equation of form like
    Ruled surface: Obtained by joining two or more space curves by means of straight lines. For any two curves say and , a generalising equation of a ruled surface is like

## Slide 59: Geometry of surface
  Synthetic surface (sculptured surface) is built using many data points or curves
    Bezier surface: The Bezier surface is the direct extension of the Bezier curve. Points on a Bezier surface can, therefore, be specified as an extension of the Bezier curve.
    where represents the rectangular array of control points (m + 1) × (n + 1) defining the vertices of the characteristic polyhedron of the Bezier patch.

## Slide 60: Geometry of surface
    B-spline surface:
    where are the control points and these form the polyhedron of the resulting B-spline surface. The surface has a degree of (k – 1) in the u direction and (l – 1) in the v direction. Knot vectors in both u and v directions are constant but not necessarily equal. The basis functions are the same as B-spline curves.
https://reference.wolfram.com/language/ref/BSplineSurface.html

## Slide 61: Geometry of surface
    Coons surface: Utilises closed intersecting boundary curves to generate a surface. For a four boundary curves r(u,0),r(0,w),r(u,1),r(1,w). Every opposite boundaries can be generated a ruled surface. A method to produce a Coons surface is superposition of two ruled surfaces.
    for ruled surfaces we have
    the final version of Coons surface patch is

## Slide 62: Solid Modelling
The most common methods used in commercial CAD system
Boundary representation (B-Rep)
Constructive Solid Geometry (CSG)
Sweeping

## Slide 63: Boundary representation (B-Rep)
Any solid occupies a limited space, that is, it has a boundary wrapped itself. By boundary, it can be clearly distinguished wherever is interior or exterior of the solid. Which means a solid can be defined by its boundary.
Usually, a boundary is geometrically described by its vertices, edges loops, faces, genus and bodies.
There are some data structures with maps have been developed for boundary representations.
Modern systems introduced also quadrics and NURBS surfaces as a part of B-Rep.

## Slide 64: Boundary representation (B-Rep)
In a B-Rep model, there are two types of information included, topological and geometric data. The topological part provides the relationships among vertices, edges and faces, etc. Geometric information is usually equations of the edges and faces.
Euler’s law
where are the number of faces, edges, vertices, face’s inner loop, bodies, and genus respectively.
B-Rep of a cylinder
(P N Rao, CAD/CAM: Principles and Applications,3e)

## Slide 65: Constructive solid geometry (CSG)
CSG is one of a fundamental theories of varies 3D modelling CAD system.
Boolean operations of multi-bodies
  One of ideas in CSG is that some algebraic calculations can be performed between two bodies.
  There are three basic Boolean operations of bodies, which are named union, difference and intersect, derived from set theory. However, in Solidworks, they are called add, subtract and common, respectively.
  Through Boolean operations one can take uses of several bodies to generate a new body.

## Slide 66: Boolean operations in set theory
In set theory, we have

## Slide 67: Boolean operations of multi-bodies
Target: The body with the finished geometry is called the target;
Tool: The body used to create or edit the shape is called the tool.

## Slide 68: Boolean logic with binary tree
A binary tree structure is usually used to store the basic bodies one lead nodes, the operations on the internal nodes, and the final body on the root node.

## Slide 69: Sweeping
A solid is created by moving a profile shape along a specified path. Most of commercial CAD systems provide the functionality for constructing swept solids in a 2D cross-section moving on a space trajectory.

## Slide 70: Three methods to create 3D models

## Slide 71: Primitive method
  In the method, any 3D model was divided into several simple, basic, standard of items, such as blocks, cylinders, spheres, cones, etc. which usually integrated in CAD system as a standard body. Through these, user can decide how to combine different of them together to construct a new model, then using Boolean operations to get the final result.

## Slide 74: Feature method
  Let user to utilize some predefined feature generating instruments, like groove, hole, slot, boss, pad, etc. to simulate a real manufacturing process to create some structure from a simple basic body.

## Slide 75: Sketch method
  The main idea of this approach is to create 3D body by 2D sketch. Taking use of extrusion, revolution algorithms, in addition some of basic Boolean operations, use can create a very complex 3D structures.
  This method is the most popular way used by most of commercial CAD softwares including Solidworks.

## Slide 76: Sketch method
The main steps of sketch method to create 3D models are
  Define a sketch plane as cross section;
  Sketch 2D shapes on the cross section;
  Constraint 2D shapes with accurate dimensions;
  Perform 2D to 3D operations.

## Slide 77: Key disciplines of modelling in Solidworks

## Slide 78: Key disciplines of modelling in Solidworks
For basic bodies, generate 3D model by taking use of 2D shapes;
Combine basic bodies to create a complex body;
Repeated bodies can be made through array operations;

## Slide 79: Coordinate system
Coordinate systems are the most important concept in a CAD system. They are used to input, store, and display geometric model. There are three kinds of coordinate systems, that is, model coordinate system (MCS), working coordinate system (WCS), and screen coordinate system (SCS).
By default, there are already a coordinates system provided for user by SOLIDWORKS every time you open a new modelling project. Usually, at the lower-left corner of the canvas, you can notice the symbol of coordinate system with three axes.
Whenever user need to carry on some location or orientation related modelling steps, the coordination system should be considered.
For example, in the scenarios of re-oriented a model or two models comparing user should define his own reference coordinate systems.

## Slide 80: References objects
Reference points
Reference vectors/axes
Reference plane

## Slide 81: Sketch
Plane curves
Two types of Constraint
  Dimensional constraints: length and angle
  Geometric constraints: parallel, perpendicular, normal, tangent, concentric, etc.

## Slide 82: CAM

## Slide 83: NC in CAM
NC, short of Numerical Control, is introduced into manufacturing field with the rapid development of microelectronics. Bendix Corporation built the first commercial production-based NC unit using MIT patents in 1954.
Basically, a NC machine runs on a program fed to it. The program consists of precise instructions with geometric and process information, such as what tool to be used, at what speed, at what feed and to move from which point to which point in what path.
To make the soft instructions sense, some hard part should be driven
  starting and stopping of machine-tool spindle
  controlling the spindle speed
  positioning the tool tip at desired locations and guiding it along desired paths by automatic control of the motion of slides
  controlling the rate of movement of the tool tip
  changing of tools in the spindle

## Slide 84: Developments of numerical control
The first-generation NC machine tools was developed from MIT in 1952. It used only digital electronic circuits and didn’t contain any actual central processing unit.
In the 1970s, computer numerically controlled (CNC) machine tools were developed with minicomputers as control units.
Today’s CNC systems use high performance microprocessors and programmable logical controllers, which allow simultaneous servoposition and velocity control of all the axis and have capable of an extended range of machining operations, such as machining centres, turning centres, mill-turning centres, CNC grinding, CNC spark erosion etc.

## Slide 85: Principle of numerical control
The basic information that has to be input into the system consists of the part geometry, cutting-process parameters followed by the cutting tools used.
The part program is then entered into the controller of the machine, which in turn runs the machine tool to make the part.
Each of the machine axes is connected to a servomotor/stepmotor which works under the control of the Machine Control Unit (MCU).
The movement of the cutting tool with respect to the workpiece is given in terms of the coordinates, which are used to control the motion of the servomotor/stepmotor which drives the individual axes.

## Slide 87: Principles of a CNC Servo System
Usually, a CNC servo system works in the digital mode, which means its control signal is with the form of electrical pulses.

## Slide 88: Main types of CNC machine
Computer Numerical Control (CNC) integrated a computer type controller into the machine tools, which is a big step from NC to CNC. NC focuses mainly on the hardware techniques, and on the other hand, CNC mainly concerns of software techniques, which means more flexibilities, huge data throughput, standard OS. Sometimes it is also termed software numerical control.
There are four numerical control modes:
  Point-to-point mode; the machine tool can be moved to any point along X and Y axes, then to perform machining in Z axis at that point, such as drilling machines.
  Point-to-point straight line mode; Improved the point-to-point mode, in which the machine tool can carry out a continuous motion in each of the axis direction.
  2-axis contouring, with switchable plane; Based on the previous two modes, in this mode, the machine tool can be moved simultaneously in any 2 axes. Based on this mode, the remained one axis can only carry out motion after the 2-axis motion finished, usually we call this situation 2.5D mode.
  3-axis contouring continuous path. This mode can be found in most of current-day control systems. In this mode, the machine tool is supposed have the capability of simultaneous 3 or more axes motion.

## Slide 89: Main types of CNC machine

## Slide 90: Main units of a CNC machine tool
A typical CNC machine tool has six main units:
  Input device
  Machine control unit (MCU)
  Machine tool (actuation unit)
  Driving system
  Feedback devices
  Display unit

## Slide 91: Structure features of CNC machine
Spindle
  Spindle is the most import performing mechanism in a CNC machine-tool
  During working, a spindle usually suffers axial and radial forces which transmitted from the machining force. The accuracy of spindle should be taken care of to ensure the proper designed tolerance could be achieved.
  The requirements to keep spindle working in a best status
    High static and dynamic stiffness
    High running accuracy
    High axial and radial load carrying capacity
    Thermal stability(e.g. introducing temperature compensation system)

## Slide 92: Structure features of CNC machine
Drives
  Spindle Drives: supply power for spindle to cut.
    Dc motor, with infinitely variable speeds controlled by varying the voltage.
    Ac motor, controlled by varying the frequency. For positioning the spindle axis, ac drive is a good choice like in turn mill centres.
  Feed Drives: supply power for the motion along different axis.
    Stepper motor, A type of digital input-output device for precision starting and stopping. It can turn through a fraction of a rotation at a time. Most stepper motors run open-loop, and the faster is turns the less torque it can provide.
    Servomotor, A rotary actuator that allows for precise control of angular or linear position, velocity and acceleration. It consists of a suitable motor coupled to a sensor for position feedback. It always works under a closed-loop control mode.
    Linear motor, A recently developed drive, which works with very high speed and acceleration and very fast response.

## Slide 93: Structure features of CNC machine
Actuation Systems
  Lead Screws: a set of mechanism converts a rotary motion from the drive motor to a linear motion in a fast speed and very low friction.
  Linear-Motion Systems : used to control the direction of a translational movement of the table on which the tools or works are held. The shape and size of the work produced depends not only on the accuracy of the amount of movement, but also on the direction of the relative movement of the tool and the work.

## Slide 94: Structure features of CNC machine
Feedback Devices
  Optical Rotary Encoder: converts the rotary motion into a sequence of digital pulses. The pulses are counted to convert to either absolute or incremental position measurement.
  Linear Scale: detect a distance to get the exact position of the detecting target. Sometimes, a Moire fringe pattern will be used to magnify a very small distance.

## Slide 95: Axes and motion of a CNC machine
Coordinate system of CNC machine tools
  ISO/R841 is one of popular standards followed by most of CNC machine vendors.
  Right hand Cartesian coordinate system
  Using right hand rule to find the directions of axes and the positive direction for rotary motions.
  Usually, in order to create a coordinates the Z axis should be defined first.

## Slide 96: Axes and motion of a CNC machine
Z Axis and Motion Direction
  The definition of Z axis depends on three cases:
    In the general case of machine with spindle, the Z axis motion will be defined alone the spindle axis and the positive Z direction is letting the tool moving away cutting surface. (which means when the drill tool drilling into a workpiece, it is moving in the negative Z direction)
    In the case of machine without spindle, the Z axis motion will be defined alone the line perpendicular to the work-holding plane. And the direction is same as the first situation.
    If there is a machine with several spindles, the Z axis motion will be the same as the principal spindle which usually be identified as the one perpendicular to the work-holding surface. Meanwhile the tool motions alone the other spindles are called as secondary or tertiary motions, which can be marked as U, V, W or P, Q, R.

## Slide 97: Axes and motion of a CNC machine
X Axis and Motion Direction
  The X axis will be chosen to perpendicular to the Z axis which is already well defined, and to be usually horizontal and to put into the positioning plane of the cutting tool or the workpiece.
  The direction of the X axis motion is always to the right if looking from the principal spindle to the column.
Y Axis and Motion Direction
  After you have got the detail of the Z and X axis, by using right hand rule people can find easily the proper Y axis and its positive direction because these three axes form a complete right-hand Cartesian system.

## Slide 98: Axes and motion of a CNC machine
Rotary Motions A, B and C
  Usually, the rotary motions with the axes X, Y and Z are termed as A, B and C respectively.
  Positive directions of A, B and C are in the directions which satisfy right-hand rule in the positive directions of X, Y and Z.

## Slide 99: Axes and motion of a CNC machine
Some examples of different axes CNC machines
Three-axes CNC machine
Four-axes CNC machine
Five-axes CNC machine

## Slide 100: CNC Tooling Systems
A tooling system define a set of configurations to mount, locate cutting tools securely in position.
A typical tooling system should meet some requirements as follows:
  Easily manipulated by a tool changing mechanism
  Keep repeatability within tolerance of a tool
  Fast and easy tool assembly
Most of configurations of them are following ISO standard. Statistically, the 20-30% of total budget was spent on tooling for a NC machine tools. It is always a key to get the exactly position of a tool tip at any time in any machining process.
Origin: https://en.nttool.com/products/nc/
Flanges
Collets

## Slide 101: Cutting Tool for CNC Machine Tools
Features a cutting tool must have
  Hot hardness: must maintain its strength and hardness during cutting processing even experience in high temperature situation.
  Toughness: can not be made broken or crack when cutting status changing suddenly.
  Wear resistance: a relative longer life before be replaced

## Slide 102: Cutting Tool for CNC Machine Tools
Commonly used cutting tool materials
  High speed steel (HSS): is a complex carbides of tungsten, molybdenum and chromium, which has the highest toughness, high hot hardness and good wear resistance
  Cemented carbides: produced by the cold compaction of the tungsten carbide powder in a binder. when coated they get superior properties.
  Ceramics: are essentially alumina-based high refractory materials, which has highest wear resistance but low toughness.
  Diamond: is essential pure carbon with two types: industrial grade natural diamonds and synthetic polycrystalline diamonds.
  Cubic boron nitride (CBN): similar to diamond, also has polycrystalline structure bonded to a carbide base.

## Slide 103: Cutting Tool for CNC Machine Tools
Commonly used cutting tool materials
Tool material | Suitable working materials and conditions
Carbon steels | Low strength, softer materials, nonferrous alloys, plastics with low cutting speeds
High-speed steel | All materials of low and medium strength and hardness. Can not be used at high rate of metal removal
Cemented carbide | All materials up to medium strength and hardness. Not suitable for low-speed application
Ceramics | Cast iron, Ni-base super alloys, nonferrous alloy, plastics. Not suitable for low speed operation or interrupted cutting
Diamonds | Can only be used on nonferrous metals because carbon has an strong affinity with ferrous metals.
CBN | Only be used in some extreme cutting conditions

## Slide 104: Comprises of a CNC system
Based on this structure, there are serval commercial systems working on the different CNC machine tools all over the world. Systems developed by Fanuc and Siemens are most famous two.

## Slide 105: CNC control systems
Fanuc CNC Series (30i like…)
  Very popular control systems developed by FANUC and GE Fanuc Automation
  Multiple axes (up to 40 axes and 24 of which can be interpolated simultaneously) and multipath (up to 10 paths) support, such as
    Multi-axis lathes
    5-axis machining centers
    Gear cutting machines
    Transfer machines
  Integrated PLC/PMC(Programmable Machine Control)
  Easy to create HMI screen

## Slide 106: CNC control system
Siemens Sinumerik series (SINUMERIK 840 like)
  Drive-based high-performance NCUs (Numerical Control Units),
  Up to 93 axes in 30 machining channels to be controlled in the NCU link
  Can be integrated completely in the Totally Integrated Automation (TIA) Portal using PROFINET.
  Suitable for turning, milling, grinding, nibbling, laser machining and gear wheel machining.
  DXF files can be directly opened on the CNC, and transferred to the CNC program.
  Tool geometries and work offsets are corrected automatically so that the required production tolerances are maintained.
  Tool data and magazine location information are clearly stored.

## Slide 107: Introduction to CAPP
Three important process parameters
  Cutting velocity/speed: the kernel parameter in three, it is a relative speed difference between the tool and workpiece, which defines the main cutting motion.
  Feed rate: usually perpendicular to the direction of cutting velocity. It helps cutting tool to form a 2D surface of material.
  Depth of cut: specifies the thickness of the surface above mentioned, which finished the total volume definition of material cut.

## Slide 108: Introduction to CAPP
Three important process parameters
  All those three parameters defined well how much material will be removed by cutting tool in an unit period of time, which is usually named the metal removal rate.
  Usually, cutting speeds are selected for a specified tool life. Higher the cutting speed, shorter will be the life of the tool.
  A high depth of cut will result in higher metal removal rate and less time for machining, resulting in low machining cost.
  Higher feed will also reduce machining time and therefore, machining cost. However, the increase in feed will affect the tool life more than increasing depth of cut.
  It is advisable to select a higher depth of cut and smaller feed for the same chip cross-section. In finishing it is necessary to select small depth of cut and feed.

## Slide 109: Introduction to CAPP
Principles for process design
  What a process design concerns is how to change a piece of designed drawing on paper or in a computer into a real physical entity. To do this, there are bunch of things a process designer should take into account. Like
    Analysis of part requirements.
    Selection of raw workpiece/material.
    Determination of manufacturing operations and their sequences.
    Selection of machine tools.
    Selection of tools, work-holding devices and inspection equipment.
    Determination of machining conditions (cutting speed, feed and depth of cut) and manufacturing times (setup time, processing time and lead time).

## Slide 110: Introduction to CAPP
Principles for process design
  The above-mentioned steps are not always performed sequentially, they are inter-connected.
  Even for the same model, there could be several methods to produce it. Each of which spends different time and cost. And the quality, accuracy, and productivity heavily depend on the process performed.
  Usually, a well designed process refers to a set of instructions that translate design specifications into manufacturing process details. If all the process was followed, a design specifications will be met.

## Slide 111: Introduction to CAPP
Computer-Aided Process Planning
  Definition
    Traditionally, process planning is performed manually by highly experienced planners who possess in-depth knowledge of the manufacturing processes involved and the capabilities of the shop-floor facilities.
    Computer Aided Process Planning ( CAPP) is a means to automatically develop the process plan from the geometric image of the component. The key to development of such CAPP Systems is to structure the data concerning part design, manufacturing facilities and capabilities into categories and logical relationships.
    CAPP appears to fully integrate CAD and CAM

## Slide 112: Introduction to CAPP

## Slide 113: Introduction to CAPP
Computer-Aided Process Planning
  Variant Method
    Search for a generic process plan from the existing master process plans developed for each part family and edits to suit the requirement of the part. The variant Method is commonly implemented with Group Technology (GT) coding system. Here, the parts are segmented into groups based on similarity and each group has a master plan.
    Four-step process
      define the coding scheme;
      group the parts into part families;
      develop a standard process plan;
      retrieve and modify the standard plan.

## Slide 114: Introduction to CAPP

## Slide 115: Introduction to CAPP
Computer-Aided Process Planning
  Generative Method
  Process plans are generated by means of decision logic, formulas, technology algorithms and geometry-based data to uniquely perform processing
  decisions. The knowledge-based CAPP system is most commonly used. It refers to a computer program that can store knowledge of a particular domain and use that knowledge to solve problems from that domain in an intelligent way. In such a system, computers are used to simulate the decision process of a human expert.
  There are two major problems to be solved: knowledge representation and inference mechanism.

## Slide 116: Programming for CNC machining
Review of coordinate systems of CNC
  The machine tools are programmed in a Cartesian coordinate system.
  The Z axis is always aligned with the direction of spindle. The primary X motion is normally parallel to the longest dimension of the primary machine tool table. The Y axis is normally parallel to the shortest dimension of the primary machine tool table. Characters A, B, and C designate angular motions around the X, Y, and Z axes, respectively.
  A programmer can always assume that the tool moves relative to the coordinate system of the stationary workpiece.
Manual part
Computer assisted part programming
  Basics of Analytical Geometry
  APT Part Programming Language
  Trajectory Generation

## Slide 117: Programming for CNC machining
CNC part programming with CAD system.

## Slide 118: Programming for CNC machining
An NC part program represents the machining sequences, or blocks, used to produce a desired component shape. Each block starts with the letter N followed by the block sequence number. One block of a typical NC program would look like
N0040 G91 X25.00 Y10.00 Z−12.55 F150 S1100 T06 M03 M07
The NC program consists of blocks, and each block consists of several words. A word starts with a character followed by numbers that represent a speciﬁc command for the machine tool.

## Slide 119: Programming for CNC machining
Basically, Most of NC words and their functions follows ISO 1056 international standards.
The word starting with G represents the preparatory functions, and the M words are the miscellaneous functions in the NC program. The words starting with F and S represent the feed and spindle speeds, respectively. T represents the tool number. x, y, and z letters followed by the scalars represent the motion lengths in the designated axes.

## Slide 120: Programming for CNC machining
Based on this, the red NC block given above is interpreted as follows by the CNC executive software:
  Load tool number 6 on the spindle (T06).
  rotate the spindle CW at 1100 rev/min (S1100,M03) and turn the cutting ﬂuid on (M07) before the motion starts.
  Move the machine tool in 25mm, 10mm, and 12.55mm increments (G91) in the x, y, and z directions with the resultant feeding velocity of 150 mm/min along the tool path.
  N040 represents the 40th block sequence of the entire part program.

## Slide 121: Programming for CNC machining
Commonly used NC words are as follows:
NC word | Description | NC word | Description
N | Block sequence number | C | Angular dimension about Z axis
G | Preparatory function | I | Interpolation parameter or thread lead parallel to X
X | Primary X motion dimension | J | Interpolation parameter or thread lead parallel to Y
Y | Primary Y motion dimension | K | Interpolation parameter or thread lead parallel to Z
Z | Primary Z motion dimension | F | Feed word
U | Secondary motion parallel to X axis | M | Miscellaneous function
V | Secondary motion parallel to Y axis | S | Spindle speed word
W | Secondary motion parallel to Z axis | T | Tool number word
A | Angular dimension about X axis | R | Rapid traverse dimension in Z axis
B | Angular dimension about Y axis |  | 

## Slide 122: Programming for CNC machining
Some commonly used CNC Functions

## Slide 123: CNC operations
Absolute programming:
  – absolute coordinates are given in the machine’s coordinate space
  – the origin may be redefined
Incremental programming:
  – each move is specified as an increment from the previous position
  – the encoders must be moved to a known position at start-up
Cutter compensation (Tool Nose Radius Compensation):
  – most tools cut on a curved edge rather than single point
  – the cutter path must be offset by the tool radius; the path defines the tool side of profile
  – using a different tool should not affect the program
Constant surface speed (CSS)
  – this automatically adjusts the spindle speed to maintain the cutter speed with respect to workpiece

## Slide 124: Machining from 3D models

## Slide 125: Material handling in CAM environment
Logistic and storage system
  AGVS
  AS/RS
  Swarf handling and disposal of wastes
Assembly lines
  Quantitative analysis of assembly systems.

## Slide 126: Key disciplines of manufacturing under Solidworks environment
Configuration for a mill or turn machine
Features to machining strategy
Generate operation plan
Generate tool path
Simulation
Post process

## Slide 127: The following slides are only for learning purpose

## Slide 128
Create a new part
Check the unit setting
Using sketch to create part body
  Smart dimension is an import tool to drive the model creatation

## Slide 129
Go to the Solidworks CAM module(just perform each of tool button alone the toolbar from left to right, one can finally get the tool path and G-codes)
  Define machine
  Setup coordinate system
  Define stock size using stock manager

## Slide 130
  Using setup->mill setup to tell the machine which direction is the machining (removing material) direction.
  Extract machinable features(which features will be removed)
  Generate operation plan(usually have cutting times for the same surface)
    Adjust the plan by removing part of operations or changing some parameters for cutting
    How to decide the basic cutting parameters(F/S):
      Cutting and spindle speed calculations

## Slide 131
          Feed rate calculatons
            Ususlly, we have general start conditons, in which
            For HSS(high speed steel tool)

## Slide 132
        For Carbide
        Depth of cut is approximately 10% the diameter of the tool, except with face mills:0.005 inch max. (SFPM=surface feet per minute)
      Decide roughing